## Slide 1: How to Handle “Engine Won’t Start” Issue
When your Aventro vehicle’s engine refuses to start, it can be frustrating. Use this step-by-step guide to help diagnose and resolve the problem, or to gather information before contacting an Aventro Service Center.

## Slide 2
1. Check the Basics
Gear Position: Ensure the car is in ‘Park’ (automatic) or ‘Neutral’ (manual).
Steering Lock: Gently turn the steering wheel while turning the key if steering is locked.
Key/Start Button: Switch ignition off and retry. For push-button start, press brake/clutch while starting.

## Slide 3
2. Battery Check
Symptoms: No lights/display, slow/absent cranking sounds, clicking noise.
Actions:
  Inspect dashboard for dim or no lights.
  Try using headlights or infotainment; if dim or off, battery may be the culprit.
  If available, try jump-starting with a healthy battery.
  For Electric variants: Ensure Battery Pack has adequate charge. Attempt Fast Charging if possible.

## Slide 4
3. Fuel System Inspection
Low Fuel/Empty Tank: Check fuel gauge and fill if necessary.
Diesel Vehicles: Ensure there’s no air lock or recent filter change.
Hybrid/Electric: Ensure main battery charge is sufficient.

## Slide 5
4. Starter Motor & Electricals
Symptoms: Single click or silence, even with good battery.
Actions:
  Check for blown fuses (refer to user manual location).
  Test if interior lights stay bright when key is turned; if yes, suspect starter relay/motor.

## Slide 6
5. Check Engine Warning Lights
Look for: Engine/Malfunction lights on dashboard.
Action: If warning lights appear, note down symbol/color for service personnel.

## Slide 7
6. Listen for Sounds
Rapid Clicking: Battery/starter issues.
Engine Cranking (but not starting): Possible fuel, ignition, or electrical problems.
No Sound at all: Battery, ignition switch, or starter.

## Slide 8
7. Check Engine Components
Loose Battery Terminals: Tighten if needed.
Corroded Terminals: Clean carefully.
Fuses: Replace if blown (carry spare fuses if possible).
Relays: Swap with identical relays if available for testing.
Security Systems: Deactivate aftermarket alarms/immobilizers, if installed.

## Slide 9
8. Call Aventro Roadside Assistance
If the car still won’t start after these checks, contact Aventro Roadside Assistance:
  Location: Find nearest Aventro Service Center.
  Helpline: +91 124 1234567