## Slide 1: How to Tow Your Aventro Car
Whether you’ve had a breakdown, a minor accident, or just need to move your Aventro vehicle, towing it safely is critical. Below is a step-by-step guide for both manual and automatic Aventro car models.

## Slide 2
Before You Begin
Check Owner’s Manual: Refer to your specific model’s owner’s manual for any towing restrictions or recommendations.
Warning! Never tow with wheels on the ground if your model is electric. Use a flatbed truck.

## Slide 3
Step 1: Gather Necessary Tools
Tow strap or tow rope (rated for your car weight)
Tow hook (provided with vehicle, usually in trunk/tool kit)
Torch (for visibility at night)
Warning triangle or cones

## Slide 4
Step 2: Locate the Tow Hook Covers
Front and Rear Bumper:
  Look for small plastic covers on the bumper (often marked by a tow symbol).
Remove the Cover:
  Use a plastic pry tool or key to open the cover.

## Slide 5
Step 3: Attach the Tow Hook
Retrieve the Tow Hook:
  Found in your car’s tool kit or trunk.
Screw in the Tow Hook:
  Insert into the exposed thread & rotate clockwise until tight.

## Slide 6
Step 4: Connect the Tow Strap or Tow Rope
Attach to Tow Hook: Ensure the strap/rope is securely fastened to the tow hook.
Other Vehicle: Attach the other end to the towing vehicle’s tow point.

## Slide 7
Step 5: Prepare the Vehicle for Towing
Manual Transmission: Place in Neutral, release the parking brake.
Automatic Transmission: Place in Neutral (N), release the parking brake. CAUTION: For automatics and hybrids, flatbed towing is recommended to avoid transmission damage.
Electric Vehicles: ONLY FLATBED TOWING. Do not tow with wheels on ground.

## Slide 8
Step 6: Safety Measures
Place warning triangle/cones at a safe distance behind both vehicles.
Switch ON hazard lights on both vehicles.
Ensure both drivers agree on signaling and communication.

## Slide 9
Step 7: Towing
The towing vehicle should accelerate slowly – no sudden jerks.
Maximum speed should not exceed 25 km/h.
Keep the towed vehicle’s ignition ON (to prevent steering lock and allow brake assist).
Steer and brake gently in the towed vehicle.

## Slide 10
Step 8: After Towing
Park both vehicles safely.
Unscrew the tow hook and store it back with your tools.
Replace the plastic tow hook cover.

## Slide 11
Important Safety Notice
Never tow on highways unless necessary.
Do not allow passengers in the towed vehicle.
If in doubt, use Aventro Roadside Assistance or professional towing.

## Slide 12
Contact Aventro Motors Roadside Assistance
Phone: +91 124 1234567
Email: info@aventromotors.com

## Slide 13
For model-specific instructions, always refer to your Aventro Owner’s Manual.